## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg

## Slide 2: What is the confusion regarding dB, dBm?
What does unit dB mean? A unit of measurement that expresses ratio of one quantity to another. Commonly used for measuring sound waves, wireless signals, communication systems and electrical signals.
How do you calculate? When the quantity is mentioned in power
  dB=10×log10​(P2 / ​P1​​)
    P2 is being measured against P1

## Slide 3: What is the confusion regarding dB, dBm?
What does unit dB mean? A unit of measurement that expresses ratio of one quantity to another. Commonly used for measuring sound waves, wireless signals, communication systems and electrical signals.
How do you calculate? When the quantity is mentioned in amplitude
  Factor 20 accounts for power being expressed as a square of amplitude
  dB=20×log10​(A2/ ​A​1)
    A2 is being measured against A1

## Slide 4: What is the confusion regarding dB, dBm?
dBm: The power of a signal in decibel and relative to one milliwatt
  What is 0 dBm? It is exactly one milliwatt
How do you calculate?
  dBm=10×log10​(P/ 1mW​)
  Measuring quantity P (expressed in milliwatts also)
Commonly used in communication and embedded systems

## Slide 5: Examples
Question: A wireless communication system involves increasing the transmit power from 1 Watts to 10 Watts. Can you estimate what is the increase in power when expressed in dB?
Answer: P1 = 1 Watt; P2 = 10 Watt
Increase in transmit power for communication system
= 10 X log10​(10/1) = 10 dB

## Slide 6: Examples
Question: A transmitter is radiating signal of strength of power output of 50 milliwatts. Can you estimate the radiated signal strength in dBm?
Answer: dBm=. 10×log10​(P/1 mW), P = 50 milliwatt
= 10×log10​(50 mW/1 mW)
= 10×log10​(50)
= 10 X 1.698
= 16.98 dBm

## Slide 7: Examples
Question: A transmitter is radiating signal of strength of power output of 50 milliwatts. Can you estimate the radiated signal strength in dBm?
Answer: dBm=. 10×log10​(P/1 mW), P = 50 milliwatt
= 10×log10​(50 mW/1 mW)
= 10×log10​(50)
= 10 X 1.698
= 16.98 dBm

## Slide 8
Can you add or subtract two terms together? dB and dB, dB and dBm, dBm and dBm? When can we do this?

## Slide 9: What kind of operations can you perform?
Can you add two terms together?
  dB and another dB term
  Sure! No Issues
Question: A wireless communication system involves increasing the transmit power from 1 Watts to 10 Watts, and then increasing from 10 Watts to 100 Watts. Can you estimate change in dB?
Answer: P1 = 1 Watt; P2 = 10 Watt, P3 = 100 Watt
dB1 = 10 X log10​(10/1) = 10 dB, dB2 = 10 X log10​(100/10) = 10 dB
Resulting gain in dB = dB1 + dB2 = 20 dB
dB3 = 10 X log10​(P2/P1) = 10 X log10​(100/1) = 20 dB

## Slide 10: What kind of operations can you perform?
Question: A wireless communication system involves increasing the transmit power from 1 Watts to 10 Watts, and then increasing from 10 Watts to 100 Watts. Can you estimate change in dB?
dB units represent logarithmic ratios, adding them is Okay.
X10 Gain (10 dB)
X10 Gain (10 dB)
1 Watt
10 Watt
100 Watt

## Slide 11: What kind of operations can you perform?
Can you add two terms together?
  dBm and another dBm term
  NO!
Question: A wireless communication system involves increasing the transmit power from 50 milliwatts by another 50 milliwatts, what is resulting increase in dB and final strength in dBm?
Answer: P1 = 50 mW, Increase = 50 mW, P2 = 100 mW
P1 = 50 mW, 16.98 dBm, Increase of 50 milliwatt, We just cannot add P1 (dBm)+P1 (dBm)+ to get resulting signal strength. Poutput != 34 dBm
dBm (Final)= 10×log10​(P2/1 mW)
= 10Xlog10​(100 mW/1 mW) = 20 dBm

## Slide 12: What kind of operations can you perform?
Can you add two terms together?
  dBm and another dBm term
  NO!
Question: A wireless communication system involves increasing the transmit power from 50 milliwatts by another 50 milliwatts, what is resulting increase in dB and final strength in dBm?
Reason why we cannot add: This operation is not meaningful because dBm represent absolute power levels measured against a fixed reference (1 milliwatt). If you need to combine powers (dBm), you need to convert them to linear scale (milliwatts), add them, and convert back to dBm if needed.

## Slide 13: What kind of operations can you perform?
Can you add two terms together?
  dBm and another dB term
  Yes, it works.
Question: A wireless communication system involves increasing the transmit power from 50 milliwatts by another 50 milliwatts, what is resulting increase in dB and final strength in dBm?
Answer: P1 = 50 mW, Increase = 50 mW, P2 = 100 mW
P1 = 50 mW, 16.98 dBm, Increase of 50 milliwatt in dB is: 10log10(2) -3.01 dB
dBm (Final)= 16.98 dBm + 3.01 dB
= 20 dBm

## Slide 14: What kind of operations can you perform?
Can you subtract two terms together?
  dBm and another dBm term
  Sort of yes! Resulting value is in dB for loss,
Question: A wireless communication system involves decreasing the transmit power from 50 milliwatts to 10 milliwatts, what is resulting decrease in dB and the final strength in dBm?
Answer: P1 = 50 mW, Decrease = 40 mW, P2 (final) = 10 mW
P1 = 50 mW, 16.98 dBm, P2 (final) = 10log10(10mW/1 mW) = 10 dBm
What is decrease in strength? 16.98 dBm – 10 dBm = 6.98 dB (OK)
You can also calculate this manually.

## Slide 15
So, what is the key takeaway? What should we do and when?

## Slide 16: What kind of operations can you perform?
Operation | Description | Example
dB + dB | Add dB values when dealing with ratios or relative gains. | 3 dB gain + 2 dB gain = 5 dB gain
dB - dB | Subtract dB values when dealing with ratios or relative losses. | 5 dB gain - 2 dB gain = 3 dB gain
dBm + dBm | Adding dBm directly is NOT valid since dBm values are absolute power levels, not relative gains. | Cannot add 30 dBm + 20 dBm directly
dBm - dBm | Subtracting dBm directly to find the ratio (in dB) between two power levels. | Difference between 30 dBm and 20 dBm = 10 dB weaker (NOT dBm)
dBm + dB | Adding dB to dBm adjusts the absolute power level by a relative amount. | 30 dBm + 3 dB = 33 dBm
dBm - dB | Subtracting dB from dBm reduces the absolute power level by a relative amount. | 30 dBm - 3 dB = 27 dBm

## Slide 17: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.